## Slide 1: PSMA-1007 (18F) injection Europian Pharmacopeia 11.4, Monograph 04/2024:3116
Anne-Fleur Lobbezoo, Ardiana Hoxhaj
PERC - Module I, Ljubljana 2025

## Slide 2: Definition, Production, Properties
Injectable, radioactive solution for PET-imaging used for diagnostic purposes of prostate cancer
Radionuclide/chemical form: PSMA-1007 (prostate specific membrane antigen) labeled with Fluorine-18

## Slide 3: Definition, Production, Properties
Production:
Fluorine-18 production with cyclotron ¹⁸O(p,n)¹⁸F
F-18 is transferred to a cassette module and trapped on an anion-exchange cartridge, where it is eluted with TBA into the synthesis module
precursor PSMA-1007 is added and the labelling reaction carried out
the with F-18 labeled PSMA-1007 is diluted with phosphate buffered saline and sodium ascorbate (stabilizer)
Appearance: clear, colourless or slightly yellow solution
Half-life: Ph.Eur. 5.7 ”Table of physical characteristics of radionuclides“
Radionuclide | Half-life | Electronic emission | Photon emission
Fluorine-18 [18F] | 109.77 min | β+ (0.250 MeV) | γ (0.511 MeV)

## Slide 4: Tests before batch release
Parameters | Method | Acceptance criteria | Reference
Identity |  |  | 
Radionuclidic purity | Gamma-ray spectometry | 0.511 MeV (sum peak 1.022 MeV) | Ph. Eur. 2.2.66 Detection and measurement of radioactivity
Radionuclidic purity | Approximate half-life | 105 - 115 minutes | Ph. Eur. 2.2.66 Detection and measurement of radioactivity
Radiochemical purity | HPLC | Retention times of [18F]PSMA in test solution and [19F]PSMA in reference solution are similar | Ph. Eur. 2.2.29 Liquid chromatography
Radiochemical purity |  |  | 
Radiochemical purity | HPLC | ≥ 91% | Ph. Eur. 2.2.29 Liquid chromatography
Radiochemical purity | TLC | Fluorine-18 ≤ 5% | Ph. Eur. 2.2.27 Thin layer chromatography

## Slide 5: Tests before batch release
Parameters | Method | Acceptance criteria | Reference
Chemical purity |  |  | 
Chemical purity (residual solvents) | GC | Ethanol: max. 10% V/V (0.790 g/ml) DMSO: max. 0.05 g/ml | Ph. Eur. 2.4.24 Identification and control of residual solvents Ph. Eur. 5.4 Residual solvents
Chemical purity | HPLC | PSMA-1007: ≤ 0.1 mg/V Other impurities: ≤ 0.1 mg/V Total: ≤ 0.5 mg/V | Ph. Eur. 2.2.29 Liquid chromatography
Chemical purity (Tetrabutylammonium) | TLC | 2.6 mg per V (V = maximum recommended dose) | Ph. Eur. 2.4.33 Tetrabutylammonium in radiopharmaceutical preparations Ph. Eur. 2.2.27 Thin layer chromatography
Chemical purity (Aminopolyether) | TLC | 2.2 mg per V (V = maximum recommended dose) | Ph. Eur. 2.2.27 Thin layer chromatography

## Slide 6: Tests before batch release
Parameters | Method | Acceptance criteria | Reference
pH | Potentiometric measurement | 4.5 - 8.5 | Ph. Eur. 2.2.3 Potentiometric determination
Bacterial endotoxins | LAL test | 175/V IU/ml | Ph. Eur. 2.6.14 Bacterial endotoxins
Particulate contamination | Visual inspection (black/white background) | no visible particles | Ph. Eur. 2.9.20 Particulate contamination: visible particles

## Slide 7: Tests after batch release
Parameters | Method | Acceptance criteria | Reference
Radionuclidic purity | Gamma-ray spectometry | Radioactivity due to radionuclide impurities ≤ 0.1% | Ph. Eur. 2.2.66 Detection and measurement of radioactivity
Radionuclidic purity | half-life | 105 - 115 minutes | Ph. Eur. 2.2.66 Detection and measurement of radioactivity
Sterility | Sterility testing | sterile | Radiopharmaceutical preparation (0125) Ph. Eur. 2.6.1 Sterility Ph.Eur. 5.5.1 Preparation of Sterile Products

## Slide 8: Storage conditions and labelling
Storage conditions: RT and protected from light.
Shelf-life: depends on the activity concentration of the product
(e.g. ABX: shelf-life of Radelumin® 10h for activity concentration of 1300 MBq/ml and 12 h for activity concentration of 2000 MBq/ml)
Labelling:
The product must contain 90% - 110% of the declared F-18 activity on the label.
activity concentration (date/time) total activity (date/time) expiration (date/time) | volume percentage of ethanol (max. 10% V/V)

## Slide 9: Deviations from the Monograph Example: Radelumin®
No test on aminopolyether (syn. Kryptofix) conducted since it is not part of the production.
Additionally: Test on sodium ascorbate performed as it is needed as a stabilizer in the product at a defined concentration (> 9 mg/ml)