## Slide 1: L-methionine ([11C]methyl) Injection
04/2023:1617
European Pharmacopeia 11th Edition
Indications: PET tracer primarily used for diagnosing and monitoring certain types of cancer mainly gliomas.
Anže Pečnik
& Francesca Kinsey
Notes: Due to the short half-life, the use of this radiotracer (as well as other 11C-based radiotracers) is limited to PET/CT or PET/MRI centers equipped with a cyclotron and a potential patient base that could benefit from this kind of study. Noteworthy, the short half-life of the radiotracer allows for limiting the exposure to ionizing radiation for the patient undergoing the diagnostic procedure

## Slide 2
11C1C4H11NO2S
Mr = 148,2
Type of decay: β+ (mean: 0.386 MeV, max: 0.960 MeV)
Half life: 20.385 min
Identification | Method | Results
Emission | Gamma-ray spectrometry | 0.511 MeV; and 1.022 MeV sum peak (depending on the measured geometry)
Approximate half life | Approximate half life determination | 18.3 min - 22.4 min
Radiochemical purity | Liquid chromatography | Examine the chromatograms obtained in the test for radiochemical purity
Sterile solution of (2S)-2-amino-4-([11C]methylsulfanyl)-butanoic acid.
Content :
– carbon-11: 90 per cent to 110 per cent of the declared carbon-11 radioactivity at the date and time stated on the label;
– methionine: maximum of 2 mg per maximum recommended dose in millilitres.
Notes: L-methionine ([11C]methyl) is a key tracer for evaluating malignant brain tumours. Malignant tumours, which have increased demands for protein and phospholipid synthesis, actively transport amino acids like methionine.
L-methionine ([11C]methyl) can help to determine the extent of the active tumour volume, classify tumour types, and monitor the effectiveness of treatments.
Target is high purity 14N often with O2 carrier gas which is irradiated with proton beam in cyclotron and resulting labelled 11CO2 gas is trapped on MS or cryotraps then released into GMP compliant synthesis module in hot cell

## Slide 3
Production:
The preparation is produced using carbon-11 derived from a gaseous target and various nuclear reactions such as proton irradiation of nitrogen. Depending on the addition of either trace amounts of oxygen or small amounts of hydrogen, the radioactivity is obtained as [11C]carbon dioxide or [11C]methane.
Possible chemical synthesis
Possible radionuclide synthesis
Notes: L-methionine ([11C]methyl) is a key tracer for evaluating malignant brain tumours. Malignant tumours, which have increased demands for protein and phospholipid synthesis, actively transport amino acids like methionine.
L-methionine ([11C]methyl) can help to determine the extent of the active tumour volume, classify tumour types, and monitor the effectiveness of treatments.
Target is high purity 14N often with O2 carrier gas which is irradiated with proton beam in cyclotron and resulting labelled 11CO2 gas is trapped on MS or cryotraps then released into GMP compliant synthesis module in hot cell

## Slide 4
Test | Method | Limit | Before release
pH | Potentiometric (2.2.3) | 4.5 - 8.5 | Yes
Sterility | Sterility test (2.6.1) | Sterile | No
Bacterial endotoxins | LAL (2.6.14) | < 175/V IU/mL | No
Chemical purity | Liquid chromatography (2.2.29) | Impurity A: ≤ 0.6 mg/V ; Impurity B: ≤ 2 mg/V ; Methionine: ≤ 2 mg/V (compared to ref. solution) | Yes
Residual solvents | Gas Chromatography (2.4.24) | max. 50 mg/V acetone | No
Radionuclidic purity | Gamma-ray spectrometry (2.2.66) | 11C ≥ 99 % of total radioactivity | No
Radiochemical purity | Liquid chromatography (2.2.29) | L-[Methyl-11C]methionine and impurity E: ≥ 95 % of radioactivity due to 11C | Yes
Enantiomeric purity | Chiral thin-layer chromatography (2.2.27) | total of L-[Methyl-11C]methionine and impurity E: ≥ 95 % of radioactivity due to 11C ; Impurity E: ≤ 10 % of the total radioactivity due to 11C | No
Notes: V being the maximum recommended dose in millilitres.

## Slide 5
A
B
C
D
E
F
Test | Method | Limit | Before release
Chemical purity | Liquid chromatography (2.2.29) | Impurity A: ≤ 0.6 mg/V ; Impurity B: ≤ 2 mg/V ; Methionine: ≤ 2 mg/V (compared to ref. solution) | Yes
Radiochemical purity | Liquid chromatography (2.2.29) | L-[Methyl-11C]methionine and impurity E: ≥ 95 % of radioactivity due to 11C | Yes
Enantiomeric purity | Chiral thin-layer chromatography (2.2.27) | total of L-[Methyl-11C]methionine and impurity E: ≥ 95 % of radioactivity due to 11C ; Impurity E: ≤ 10 % of the total radioactivity due to 11C | No

## Slide 6: Conclusion
Must also comply with monographs on Radiopharmaceutical Preparations (0125).
Speed is essential.
Current use is limited due to its physical properties and the complex production process.
Thank you for listening!