## Slide 1
Wai Hong Lo, Eddie Marius Ozenil

## Slide 2: Definition and Content
Definition
Sterile solution of sodium [1 -11C]acetate, in equilibrium with [1-11C]acetic acid
Content
Carbon-11: 90– 110% of the declared carbon-11 radioactivity at the date and time stated on the label
Acetate: maximum of 20 mg per maximum recommended dose in millilitres

## Slide 3: Production
The preparation is produced using carbon-11 derived from a gaseous target and various nuclear reactions such as proton irradiation of nitrogen
By addition of either trace amounts of oxygen or small amounts of hydrogen
The radioactivity is obtained as [11C]carbon dioxide which is used for further synthesis of sodium ([1-11C]) acetate.
Courtesy to Prof. Bert Windhorst

## Slide 4: Properties and Identification
Appearance
Clear, colourless solution
Half-life and nature of radiation of carbon-11
See general chapter 5.7. Table of physical characteristics of radionuclides
Identification
A. Gamma-ray spectrometry
  Result: The principal gamma photons have an energy of 0.511 MeV and, depending on the measurement geometry, a sum peak of 1.022 MeV may be observed.
B. Approximate half-life : 18.3 min to 22.4 min.
C. Examine the chromatograms obtained in the test for radiochemical purity
  Results: The principal peak in the radiochromatogram obtained with the test solution is similar in retention time to the principal peak in the chromatogram obtained with the reference solution.

## Slide 5: Tests
pH (2.2.3)
  4.5 to 8.5.
Sterility
  It complies with the test for sterility prescribed in the monograph on Radiopharmaceutical preparations (0125)
  The injection may be released for use before completion of the test
Bacterial endotoxins (2.6.14)
  Less than 175/V IU/mL, V being the maximum recommended dose in millilitres
  The injection may be released for use before completion of the test

## Slide 6: Tests
CHEMICAL PURITY
Acetate
Liquid chromatography (2.2.29)
Limit: acetate: Not more than the area of the corresponding peak in the chromatogram obtained with the reference solution (20 mg per V)
Residual solvents
Limited according to the principles defined in the general chapter (5.4), using the general method (2.4.24).
The preparation may be released for use before completion of the test
No chemical impurities specified

## Slide 7: Tests
RADIONUCLIDIC PURITY
Carbon-11
Gamma-ray spectrometry
Minimum 99% of total radioactivity
Limit: Peaks in the gamma-ray spectrum corresponding to photons with an energy different from 0.511 MeV or 1.022 MeV represent not more than 1% of the total radioactivity
The preparation may be released before completion of the tests
RADIOCHEMICAL PURITY
[1-11C]Acetate
Liquid chromatography (2.2.29) as described in the test for acetate
Limit: total of [1-11C]acetate: minimum 95% of the total radioactivity due to carbon-11
RADIOACTIVITY
Determine the radioactivity using a calibrated instrument.
No radiochemical impurities specified
Likely requires HPGe detection

## Slide 8: Storage and Labelling
Storage
  Airtight container
  Sufficiently shielded
Labelling
  radioactivity at a given date and time (half-life <70 days), with reference to time zone
  the route of administration;
  where applicable, the maximum recommended dose in millilitres;
  where applicable, the route of radionuclide production;
  where applicable, the concentration of ethanol and other additives;
  the name and concentration of any added antimicrobial preservative;
  where applicable, any special storage conditions
  the expiry time in clear terms (date/h/min) with reference to a specific time zone
On site preparation -> labeling can be modified
According to General Monograph 0125 - Radiopharmaceutical Preparations

## Slide 9
Wai Hong Lo, Eddie Marius Ozenil
Thank you for your attention!