## Slide 1
Iobenguane (¹²³I) injection for diagnostic use
PRESENTED BY:
Bo Yu Poupee Lam, Adam Tillo

## Slide 2
Properties
Structural similarity to norepinephrine.
Selectively taken up by adrenergic nerve terminals through norepinephrine transporters.
Labeling with ¹²³I isotope shows several advantages over 131I for imaging of tumors.
(123I-MIBG, Adreview, GE Medical)
Scintigraphy with 123I-MIBG requires a thyroid blockade.
Iobenguane (¹²³I) Injection for diagnostic use
Norepinephine
Notes: Iobenguane, or MIBG, is structurally similar to norepinephrine.
and a guanidine group which mimics norepinephrine’s terminal amine.
which makes MIBG a good ligand for the norepinephrine transporter.
It has a benzyl ring, like norepinephrine’s aromatic ring, This guanidine group is key — it stays positively charged in the body, Because of this, MIBG is taken up by adrenergic nerve terminals in the same way norepinephrine is, allowing us to use it for imaging the sympathetic nervous system and neuroendocrine tumours
Iobenguane is structuraly similar to norepinephrine. MIBG is selectively taken up by adrenergic nerve terminals through norepinephrine transporters.
This property makes it useful for imaging of sympathetic nervous system.
The tracer is labeled with gamma-emitting I-123 isotope, which has a half life of approximately 13 h. Labeling with I-123 isotope has shown advantages over I-131 in tumor imaging: lower dose to the patient, shorter time required for aquiring of the image and higher image resolution.
Thyroid blockade with nonradioactive potassium iodidde is applied during the scintigraphy to prevent excessive radioiodine uptake to the thyroid.

## Slide 3
Applications
Oncology- diagnosis and follow-up of the neuroendocrine tumors:
Neuroblastoma
Pheochromocytoma
Cardiology – assessment of cardiac sympathetic innervation.
Neurology – differentiating dementia-
Parkinson’s disease dementia (PDD), Lewy body dementia (LBD), Alzheimer’s disease dementia (AD).
Iobenguane (¹²³I) Injection for diagnostic use
Notes: The most significant use of Iobenguane concerns imaging of neuroendocrine tumors, including neuroblastoma and pheochromocytoma.
I-123 MIBG scintigraphy is essential for initial tumor staging, evaluating response to therapy and detecting recurrent disease.
Neuroblastoma is a pediatric is a pediatric malignancy arising from the symphatetic nervous system and one of the most common extracranial solid tumors in children. Pheochromocytoma is also a tumor that originates from adrenal medulla. It secretes catecholamines, leading to various clinical symptoms such as hypertension, palpitation and headaches.
Beyond neuroendocrine tumors, MIBG is also used in cardiology. Hyperactivity within the heart’s sympathetic nervous system are linked to higher risk of heart’s failure.
Furthermore, MIBG became important tool to differentiate between different forms of dementia.

## Slide 4
Production
Iobenguane (123I-MIBG) is synthesized from metaiodobenzylguanidine in an isotope exchange reaction
Iobenguane (¹²³I) Injection for diagnostic use
Central production possible due to half-life.
Synthesis: isotope exchange (MIBG + Na[¹²³I]I, ammonium sulfate catalyst).
Purification: ion-exchange resin removes free iodide.
Sterilisation: final filter.
Notes: Isotopic exhange reaction
Substrate is heatedd with Iodine 123
Purification to remove free iodide
Sterilisation
Iobenguane labelled with iodine-123 is produced centrally, rather than in the hospital, because the isotope has a half-life long enough for distribution.
The process starts with iodine-123, which is generated in a cyclotron and supplied as sodium [¹²³I] iodide. This is then reacted with metaiodobenzylguanidine, the non-radioactive precursor, in an isotope exchange reaction. A catalyst such as ammonium sulfate helps the iodide exchange occur,.
After the labelling step, the mixture is purified by ion-exchange resin to remove any free iodide, which would otherwise accumulate in the thyroid if injected. Finally, the solution is sterilised by filtration ascorbic acid is usually added as a stabiliser to prevent radiolysis
and formulated as a sterile, ready-to-use injection. and
This sequence—cyclotron production, isotope exchange labelling, purification, and sterilisation—is what the Pharmacopoeia requires to ensure a consistent, safe, and high-purity radiopharmaceutical.
Owning to the long half-life of the Iodine isotope, MIBG can be conveniently produced and supplied by radiopharmaceutical companies, therefore not requireing a local production at the hospital.
The synthetic procedure relies on a simple isotope exchange reaction between the substrate and the labeled sodium iodide in the presence of ammonium sulfate.
Purified by filtering through ion exchange resin and sterilized.

## Slide 5
  Sterile, endotoxin-free solution of 1-(3-[¹²³I]iodobenzyl)guanidine or its salts.
  May contain stabilizers (ascorbic acid), catalysts (copper ions), buffer, and preservatives.
  Contains 90–110% of stated iodine-123 activity at reference time.
  Shows a specific radioactivity of minimum 10GBq of iodine-123 per gram of iobenguane base.
Name
Definition
Iobenguane (¹²³I) Injection for diagnostic use
IOBENGUANE (123I) INJECTION
Iobenguani (123I) solutio iniectabilis
Notes: This slide shows the official definition from the European Pharmacopoeia.
Iobenguane injection is a sterile, endotoxin-free solution of 1-(3-[¹²³I]iodobenzyl)guanidine or its salts. To keep the preparation stable and effective, it may also contain ascorbic acid as a stabiliser, copper ions as a catalyst, along with buffer and preservatives.
We can then calculate the specific radioactivity which should be of min 10GBq of iodine 123 per gram
Finally, it must show a specific radioactivity of at least 10 gigabecquerels of iodine-123 per gram of iobenguane base. This ensures the preparation behaves as a true tracer — highly radioactive for imaging, but with only a very small chemical amount of drug, so it doesn’t have any pharmacological effect.

## Slide 6
Characters
Identification
Iobenguane (¹²³I) Injection for diagnostic use
  Appearance: Clear, colorless or slightly yellow solution.
  ¹²³I isotope characterized by ~13.2 h half-life and : 159 keV γ emission peak.
  Gamma/X-ray spectrometry: Confirms radionuclide (¹²³I γ peak at 159 keV).
  Chromatography (radiochemical purity test): Confirms the molecule itself is [¹²³I]-iobenguane.
5.7. TABLE OF PHYSICAL CHARACTERISTICS OF RADIONUCLIDES MENTIONED IN Eu Phr.
Notes: First, we use gamma or X-ray spectrometry to confirm the radionuclide. Iodine-123 gives a characteristic gamma emission at 159 keV which confirms we have the correct isotope.
Second, we use chromatography, as in the radiochemical purity test, to confirm the chemical identity. The chromatogram shows the peak corresponding to [¹²³I]-iobenguane, so we know the radionuclide is attached to the right molecule.
Together, these two checks prove that both the isotope and the compound are correct.

## Slide 7
Radiochemical purity
Iobenguane (¹²³I) Injection for diagnostic use
Limits:
[123I]iobenguane: minimum 95% of the radioactivity due to iodine-123;
– impurity A ([123I]iodide): maximum 4% of the radioactivity due to iodine-123;
– other impurities: maximum 1 % of the radioactivity due to iodine-123.
Notes: To check radiochemical purity, we use HPLC.
The column separates the different chemical species.
A radiodetector shows which peaks contain radioactivity, and UV at 254 nm confirms the chemical identity.
In this test, the main peak should be [¹²³I]-iobenguane.
The limits are:
At least 95% of the total radioactivity must be in the [¹²³I]-iobenguane peak.
Free iodide can be present, but no more than 4%, otherwise it would go to the thyroid.
Any other impurities must be less than 1%.
These limits make sure that almost all of the radioactivity injected into the patient is the correct tracer, giving accurate images and reducing unwanted radiation to other organs.”

## Slide 8
Tests
Iobenguane (¹²³I) Injection for diagnostic use
Notes: First, the pH must be between 3.5 and 8.0. This ensures the solution is stable and safe for intravenous injection.
Next, we calculate the specific radioactivity from the chromatogram used in the radiochemical purity test.
Here’s the important detail: the chromatogram actually measures iobenguane sulfate, but the monograph expresses results in terms of iobenguane base, the active molecule. Because the sulfate salt is heavier than the base, we apply a correction factor of 0.85 — this converts the measured sulfate value into the equivalent base value. Without this correction, we would overestimate the amount of active drug and underestimate the specific radioactivity.
For sterility, the preparation must comply with the general monograph on Radiopharmaceutical Preparations. Given the short half-life of iodine-123, the product may be released before sterility testing is complete, but the test must still be performed afterwards as a retrospective check.
Finally, bacterial endotoxins must be less than 175 divided by the maximum recommended dose volume in millilitres. This protects patients from pyrogenic reactions even when the solution is sterile.

## Slide 9
Radionuclidic purity
Iobenguane (¹²³I) Injection for diagnostic use
Notes: The monograph sets a strict limit for radionuclidic purity: all radionuclides other than iodine-123 must together be less than 0.35% of the total activity.
We check this using gamma-ray and X-ray spectrometry. Each radionuclide has a characteristic energy signal, so we can identify if anything else is present in the sample.
Typical impurities are iodine-125 and tellurium-121, which may be produced during cyclotron irradiation.
Sometimes these impurities are hard to detect because iodine-123 dominates the spectrum. For this reason, the preparation may be kept aside until most of the iodine-123 has decayed. At that point, the smaller signals from impurities become visible.
Finally, the monograph makes it clear that no long-lived radionuclides with a half-life longer than iodine-125 should be present. This ensures patients are not exposed to unnecessary radiation long after the scan.”

## Slide 10
Labelling
  Must state:
  Radionuclide (¹²³I), chemical name, pharmaceutical form.
  Total activity (MBq) and concentration at calibration date/time.
  Expiry date/time (linked to 13 h half-life).
  Specific radioactivity (GBq/g).
  Batch number, precautions (“Radioactive material – diagnostic use only”).
Notes: The monograph specifies exactly what must appear on the label.
The radionuclide, chemical name and pharmaceutical form, so the product is unmistakably identified.
The total activity in megabecquerels, and the concentration at the calibration date and time. Because iodine-123 has a half-life of only 13 hours, the expiry date and time must also be shown.
The specific radioactivity in gigabecquerels per gram, to confirm the correct ratio of radioactivity to drug.
The batch number for traceability, and the warning: Radioactive material – diagnostic use only.
Together, these labelling requirements make sure that the right product, with the right activity, is given to the right patient, and handled with the necessary radiation safety precautions.”

## Slide 11
Storage
Iobenguane (¹²³I) Injection for diagnostic use
Store protected from light
Shelf-life ≈ 1 day (t½ 13.2 h)
Prevents radiolysis and ensures correct activity
Notes: Storage conditions are simple: protect from light. Because iodine-123 has a half-life of just 13 hours, the shelf-life is limited to about one day. This prevents radiolysis and ensures the activity is accurate when administered

## Slide 12
Conclusion and Q&A